## Slide 1
Imprecise but Fun: Playful Interaction Using Electromyography
Interação Humano-Computador
Class: TP3
Jakob Karolus, Simon Thanheiser, David Peterson, Nicolas Viot, Thomas Kosch, Albrecht Schmidt, and Paweł W. Wozniak. 2022.
Imprecise but Fun: Playful Interaction Using Electromyography. Proc. ACM Hum.-Comput. Interact. 6, MHCI, Article 190 (September 2022), 21 pages.
https://doi.org/10.1145/3546725
Presented by:
Vítor Santos nº107186
Gabriel Teixeira nº107876

## Slide 2
Emergence of
Physiological
Input
Motivation
2
Potential: easy, intuitive and flexible playful interaction
Exotic input modality

## Slide 3
Introduction
3
Context
  Physiological sensing
  Insight into user's state of being
  Challenge (hard): good robustness and effective deployment
  Imprecise readings as a limitation
  Using Electromyography (EMG) to turn this limitation into a feature

## Slide 4
What is Electromyography (EMG)?
Input modality for HCI.
Computer system control with muscles
Placing electrodes on the skin (sEMG)
or
Inserting fine wire electrodes into the muscle
(EMG)
EMG measures the electrical activity of muscles
EMG
4

## Slide 5
Methodology
5
RQ1:
What are the constraints of EMG-based input for motor control?
RQ2:
How can we integrate EMG-based control as a game design element?

## Slide 6
Pilot Study
6
“EMG-BASED INPUT FOR EXPLICIT CONTROL USING A LOW-COST CONTROLLER”
Basic Steering Task
Keep a ball in line
JOYSTICK or EMG
Procedure
Stimulus screen
Strapped Electrodes
Familiarize
Repeat task for each control modality
Participants
10 total (8 m, 2 f)
Avg. Age = 26.9 y

## Slide 7
Pilot Study - Results
7
Explicit control with EMG is possible
More difficult
Less accurate
Linear mixed model

## Slide 8
Study I
Task: Soldering with steerable third hand - test fine motor control
Conditions: EMG, Pedal, Manual
Subtasks:
  Direct Control
  Free Control
8
12 participants (9 m, 3 f)
Average age 27.5 years

## Slide 9
Study I - Results
9
Accuracy: No difference
Usability and UX
Creepiness: Not particularly creepy
Comfort: Not uncomfortable
Refer to bottom graph

## Slide 10
Study II
10
“EMG-BASED INPUT IN GAME DESIGN - VROCKETBOOTS”
VR locomotion chosen:
Immersive potential
Direct muscle input as interaction with the virtual world
Naturally engaging

## Slide 11
VRocketBoots
11
Flight simulation game
Follow a given trajectory (350 m, 34 rings)
Increase altitude by standing on toes
NOTE: (non-continuous thrust !!!)
Decrease altitude on normal pose
EMG vs Controller
Why ?
Implicit control
Playful large environment traversal
Nacke et al’s guidelines:
  Direct physio. input -> virtual world action

## Slide 12
Participants
12
Composition
University recruitment
20 in total (14 m, 6 f)
Average age: 26.3 years
Standard deviation: 2.9 years
Experience
3D apps - 75%
VR - 40%
No previous study participation

## Slide 13
Procedure
13
Setup
Electrodes attached only on one leg on the calves (gastrocnemius muscle)
EMG Calibrated by performing take-off gesture
Time to familiarize
  Two flight ring practice course
Experiment
Perform flight
Short break
Switch to other condition (EMG or Controller)

## Slide 14
Results
14
Completion Time (average)
Controller: 52.8 s
EMG: 85.5 s
Flight Path Precision
Red line - Mean
Red corridor - Standard Deviation

## Slide 15
Results - Interviews
15
Preference
70% of participants preferred EMG
Challenging and immersive nature
“It was more challenging and immersive. A very different way of using controls, which made it more fun.” (P3, m, 28y)
Immersion
Reported EMG as more immersive
Challenging nature augmented fun
“It felt more like a workout. It activates more parts of my body. But it became a bit tiresome in the end.” (P9, m, 23y)

## Slide 16
Results - Interviews
16
Control
Imprecision
Break in the VR Illusion
“It felt quite natural to fly upwards, but when going in different directions it broke the illusion a bit.” (P20, m, 28y)
User insight
Continuous movement suggestion
“If it was possible to make it into a continuous movement, then it would feel like real life.” (P19, m, 25)

## Slide 17
Discussion
17
Imprecise but Fun
Bad for accuracy and completion time (RQ1)
Challenging, playful interaction through difficult muscle control (RQ2)
EMG as a Game Element
Large muscle usage
Direct mapping to game elements
Use fatigue with great care
Limitations
Fatigue
Habituation
Best muscle groups remain an open question

## Slide 18
Conclusion
18
Suggestions for EMG-based game design
Target large muscles and coarse movements
Limit design to coarse movements
Otherwise, unintended EMG input may break immersion
EMG’s Imprecision
Challenging and engaging game experiences

## Slide 19
Bibliography & Credits
18
Slide template provided by Slidesgo
Icons provided by Google Slides Add-On Flaticon
Bibliography
M.A. Cavalcanti Garcia and T.M. M. Vieira, Surface electromyography: Why, when and how to use it, Rev Andal Med Deporte. 2011;4(1):17-28